## Slide 2: The DIY Artificial Pancreas
Hacking Wetware with Open Source Software and Hardware

## Slide 3: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 4: whoami?
LAGORIO\Jay (jay@lagor.io)
B.S. Computer Science, UMBC (2008)
M. Eng. Electrical Engineering, NPS (2015)
CISSP, various SANS certifications over the years
Developer, IT Consultant, Private Investigator
  Projects at UMBC as a student, many projects thereafter
  Maryland-based Ambulance company
  Other sectors, and myself

## Slide 5: whoami?
.NET Developer
  Facebook API 1.0 library
  Workflow management (PHP too!)
  Craal
  Lots of personal projects

## Slide 7: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 8: Introduction to Diabetes
Diabetes affects nearly 200 million people worldwide and comes in two flavors
  A deficiency in the pancreas to properly produce insulin (Type I), genetic
  A deficiency in the body to absorb insulin (Type II)
We’ve all heard the meme: There will be a cure in 5 years ™
Insulin is a hormone required to sustain human life, so people with this disease must obtain it from another source
  Long acting
  Short acting

## Slide 9: Introduction to Diabetes
Administered according to a complex formula accounting for:
  Carbohydrates
  Physical activity
  Sickness
  Preexisting insulin levels
  Adrenalin
  Insulin Sensitivity
Straddle a tenuous line between their blood sugar rising too high or dropping too low.

## Slide 10: Introduction to Diabetes

## Slide 11: Introduction to Diabetes

## Slide 12: Introduction to Diabetes

## Slide 13: Introduction to Diabetes

## Slide 14: Introduction to Diabetes
…ish
You can’t measure all of these values
You don’t know that the carbohydrates are going to hit your system at the same speed as the insulin, which could cause low blood sugar
Sensitivity to insulin changes over time and is different in every person
You have to maintain safety at night while you sleep – a 24/7 disease

## Slide 15: Introduction to Diabetes
How do you measure how well you’re doing?
  An A1c blood test measures a chemical related to your glucose levels over a period of about 3 months
  In aggregate, it’s a good approximation of how close your average blood sugar has been over that time
  Blood sugar fluctuates during the day due to eating, so you have to maintain control because it affects your A1c
  Blood sugar should not fluctuate wildly during sleep, so if you do well over night you get that measurement improvement “for free” since you’re not eating while your range is maintained

## Slide 16: Introduction to Diabetes
Some technology exists to make it easier to maintain some form of control over blood sugar
  Largely go toward easing the burden of monitoring and managing symptoms
  None of these solutions take a decision-making role in management of the disease
Injections: people used to give themselves multiple injections of different kinds of insulin per day
  Use an insulin pump to both slowly dose background insulin throughout the day and to give themselves larger (but riskier!) doses required at meals
  Worn for days at a time, eliminating multiple painful injections throughout the day and reducing a lot of medical waste

## Slide 17: Introduction to Diabetes
Blood Glucose Measurement: Most patients still must use some finger sticks to draw blood to check their blood sugar
  A point-in-time measurement lacking real-world context like trend direction
Continuous Glucose Monitor (CGM): Sensor that stays attached to you for days at a time
  Takes a reading every five minutes, exposing trends
  The CGM receiver alarms when readings venture outside of pre-set parameters
  Wake the patient up at night to take needed action to raise or lower their blood sugar back to safe levels

## Slide 18: Introduction to Diabetes
No bedtime snacks, you don’t know what’s going to happen while you sleep
You intentionally go to bed on the higher end of the scale, but not too high, because your glucose will be pushed down by the unthinking insulin pump and you don’t want to alarm or wake up too low
Every meal, even meals you have often that are usually predictable, can become an hours long battle to get back to normal
Rule of thumb: If you wake up too high there is no recovery to a good state during the day

## Slide 19: Introduction to Diabetes
Notes: https://www.researchgate.net/figure/Percent-of-time-spent-in-blood-glucose-ranges-during-the-course-of-continuous-insulin_fig2_51460927
Effect of Diabetes Mellitus on Outcomes of Hyperglycemia in a Mixed Medical Surgical Intensive Care Unit
May 2011
In range defined as 80 – 180 average time spent in range is 65%

## Slide 20: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 21: Hardware
It must be restated:
None of the FDA-certified components take action on behalf of the patient and a human is still required to be in the loop.

## Slide 22: Hardware
We need to develop a solution that:
  Takes the data from the CGM
  Processes it with what it already knows about our bodies and current state
  Predicts future effects based on existing state, proposed changes, and medication calculations
  And delivers a command to an insulin pump to do something other than deliver regular, unchanging background insulin.

## Slide 23: Hardware
This requires us to overcome four technical challenges:
  We need a small, low-power and portable platform that the user can easily bring with them through their day to do all of this.
  A visualization solution that allows us to monitor the system both historically and as it works in real-time is required to monitor the status of the solution.
  We need to collect blood sugar readings from an FDA-certified CGM system.
  We need to be able to query and control an FDA-certified insulin pump.

## Slide 24: Hardware
The Raspberry Pi, particularly the Pi Zero, and Intel Edison are ultra-portable platforms that make phenomenal solutions on which to run our code
Each has built-in Bluetooth and Wi-Fi making it easy to connect them to known networks or tether them to a cell phone when not at home without needing extra attachments
We can collect CGM data over Bluetooth without having to plug the manufacturer-provided receiver into the board, although that remains an option with USB OTG

## Slide 25: Hardware
Our CGM and platform problems solved, the Open Source hardware community stepped in and created two solutions to the pump problem.
  The Explorer Board for the Intel Edison
  Explorer HAT for the Raspberry Pi
900 MHz radios that while advertised as general-purpose ISM band radios communicate with the insulin pumps using the proprietary protocol
Protocol reverse engineered by a community member over the course of several years: @bewestisdoing

## Slide 26: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 27: Software and Safety
Our visualization software solution stack:
  Node and Go
  Mongo
  Python and Bash
Nightscout is a purpose-built visualization and web-based data warehousing platform built on Mongo and Node designed specifically for remotely monitoring the well-being of a diabetic, whether yourself or those under your care.

## Slide 28: Software and Safety
Each person builds their own Nightscout instance
  Heroku or Azure, free tier plans
  You can run it on private infrastructure if you have that option available to you
Nightscout is good for point-in-time representation about things now
Also useful it to give our solution some insight into our actions so it can make treatment decisions
Serves as a great reporting tool that can be used to generate charts and reports to bring to routine medical appointments

## Slide 29: Software and Safety
The Open Artificial Pancreas System, or OpenAPS
Node, Python, Go, and Bash suite of components that runs on Linux
Designed to acquire CGM data, process it using an algorithm and deliver a dosage command to an insulin pump
  More than 1,440 people are using this around the world
  13.7M person-hours of algorithm experience combined

## Slide 30: Software and Safety
A person can be expected to do the equation just several times per day
OpenAPS processes data and can make dosing decisions every five minutes
  That’s 288 times per day
  Including, most importantly, while the patient is sleeping
Better decision making than the patient because even more can be taken into account
  Insulin Absorption Modelling: Uses the manufacturer’s equations to predict impact
  Autotune: Tunes the algorithm to carbs and insulin over weeks
  Autosens: Tunes the algorithm to your body over the last 24 hours
Advance warnings: Tells you how much to eat as a correction to keep up

## Slide 31: Software and Safety
Can normally be expected to wake up at least once or twice every night to alarms requiring action
  OpenAPS works to keep the patient in range without intervention
  Sleep is one particular area of life that improves dramatically almost immediately
A sleeping patient isn’t eating so it’s easy for the system to maintain them within range
Good time in range, especially at night, improves A1c measurement without any work on their part as well

## Slide 32: Software and Safety

## Slide 33: Software and Safety
While under development, users and maintainers have been building the plane while flying it.
Safety is a critical factor in the way changes and features are implemented because it’s important that this doesn’t cause someone to be hospitalized
  Several checks and double checks are made before making dosing decisions
  Fallback behaviors are defined
  Features that may impact the algorithm are scrutinized heavily

## Slide 34: Software and Safety
New failure modes are well defined:
  OpenAPS is out of range of the source of glucose readings
  OpenAPS is out of range of the insulin pump
  A process running on the OpenAPS device dies and needs to be restarted
  Power loss in one or more devices
Commands are delivered so the pump reverts to normal, factory behavior when one of these failure modes occurs
During sleep the manufacturer-provided CGM receiver can be used as a secondary safety system to sound an alarm if the blood sugar levels go out of a defined range

## Slide 35: Software and Safety
Normal care routines operate by making large drastic changes that can’t be undone in both carbohydrates and insulin intake
  Eating 60g of carbohydrates? That might be 6.6U of insulin
One indirect safety factor that was discovered through use of the system makes sense when thought to its logical conclusion:
  Making very small changes every five minutes allows the system to self-correct after just five more minutes if the situation should suddenly change
  Sudden rapid rise? Add more insulin
  Sudden unexpected descent? Suspend delivery

## Slide 36: Software and Safety
Key during meals: don’t take the entire insulin dose at the beginning of a meal and hope the body doesn’t process the insulin faster than the carbohydrates
  Taking the whole dose has a non-zero chance of causing low blood sugar
OpenAPS mimics the pancreas’s normal function
  Slowly doses insulin as the body processes carbohydrates, keeps the patient’s blood sugar from extremes
Lesser amounts of insulin in a person’s system at any given time reduces the overall likelihood they experience blood sugar drop

## Slide 37: Software and Safety
This requires us to overcome four technical challenges:
  We need a small, low-power and portable platform that the user can easily bring with them through their day to do all of this.
  A visualization solution that allows us to monitor the system both historically and as it works in real-time is required to monitor the status of the solution.
  We need to collect blood sugar readings from an FDA-certified CGM system.
  We need to be able to query and control an FDA-certified insulin pump.

## Slide 38: Software and Safety
This requires us to overcome four technical challenges:
  We need a small, low-power and portable platform that the user can easily bring with them through their day to do all of this.
  A visualization solution that allows us to monitor the system both historically and as it works in real-time is required to monitor the status of the solution.
  We need to collect blood sugar readings from an FDA-certified CGM system.
  We need to be able to query and control an FDA-certified insulin pump.

## Slide 39: Software and Safety

## Slide 40: Software and Safety
Older insulin pumps that have wireless connectivity allowed the manufacturer to use a proprietary protocol to communicate with the pump.
Discovered and turned into a Black Hat talk in 2013 with an emphasis toward how this could be misused
Manufacturers significantly limited how this functionality could be used on newer pumps.
This wrinkle requires us to find and purchase older, used pumps and to use custom hardware and software.

## Slide 41: Software and Safety
Medtronic stopped manufacturing pumps that were remotely controllable, but did not recall the devices
Older devices are already hard to acquire:
  eBay
  Craigslist
  Mercari
  MedWOW
Price gouging galore: started at ~$300, skyrocketed to > ~$1000
After the FDA warning about unapproved uses of medical devices, meaning CGM algorithms, another bomb drops

## Slide 42: Software and Safety

## Slide 43: Software and Safety

## Slide 44: Software and Safety

## Slide 45: Software and Safety

## Slide 46: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 47: Iterative Improvements
Several implementations built over the last three years
Assemblies range in size
  Large, requiring a shave kit bag modified to strap the components to the inside
  Small, enough to fit unnoticed in a pant leg pocket.
Each iteration and choice of component reduced the size, improved portability and battery life
  Building the plane while flying it
Contributed to OpenAPS projects adding improved compatibility with FDA-certified devices, reduced friction around installing the system

## Slide 48: Iterative Improvements
Implementation and improvement of an interactive setup script
Maximum flexibility around connectivity
The systems work without requiring a connection to the Internet when one isn’t available
When Internet connectivity returns the device drops all of the data from the time it spent disconnected into Nightscout to aid in later analysis
As long as it gets time when it starts up it doesn’t need to be connected to the Internet continuously

## Slide 49: Iterative Improvements

## Slide 50: Iterative Improvements

## Slide 51: Iterative Improvements

## Slide 52: Iterative Improvements

## Slide 53: Iterative Improvements

## Slide 54: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 55: Live Demo
Show Nightscout

## Slide 56: Live Demo
Show loop log
Show CGM log

## Slide 57: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 60: Results
Date | A1c | A1c Est
9/4/2008 | 16.5 | 
11/24/2008 | 6.2 | 
3/16/2009 | 7.0 | 
10/29/2009 | 7.1 | 
5/19/2010 | 6.9 | 
9/8/2010 | 6.9 | 
4/28/2011 | 7.1 | 
8/8/2011 | 7.2 | 
9/18/2012 | 6.6 | 
4/30/2013 | 6.9 | 
9/10/2013 | 7.1 | 
6/17/2014 | 7.3 | 
1/29/2015 | 6.6 | 
6/2/2015 | 6.7 | 
7/29/2015 | 7.2 | 
12/10/2015 | 7.5 | 
3/15/2016 | 7.3 | 
11/29/2016 | 6.7 | 6.5
8/8/2017 | 6.2 | 6.4
2/9/2018 | 6.2 | 6.4
1/22/2019 | 6.3 | 6.1

## Slide 61: Results
Industry changes
  Previously all integrated systems were monolithic systems

## Slide 62: Results
Industry changes
  Previously all integrated systems were monolithic systems

## Slide 63: Results
Industry changes
  Previously all integrated systems were monolithic systems

## Slide 64: Results
Industry changes
  Discrete CGM, pumps, and algorithms that all work without collective FDA approval
  iCGM
    Dexcom G6 is the first certified product

## Slide 65: Results
Industry changes
  ACE (Alternate Controller Enabled)
    An insulin pump, but works with an iCGM and iController
    Tandem t:slim X2 is the first certified product

## Slide 66: Results
Industry changes
  iController
    The algorithm, brings together iCGM and ACE to autopilot the plane for the patient
    No certified products yet, but Tidepool is trying to get an FDA certified version of Loop, Tandem is attempting to push an integrated TypeZero product at the end of the year

## Slide 68: Results

## Slide 69: Results
#WeAreNotWaiting

## Slide 70: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 71: Exponential Growth
Everyone needs insulin, this is a biological fact
Lack of the hormone is not a question of lifestyles, choices, or what the person could have done better
This lightning strike could happen to anyone in this room
People without it die, no question
  Just like water
  Just like air
Most have it, some don’t: creates an economic opportunity

## Slide 72: Exponential Growth
Your money or your life, kid

## Slide 73: Exponential Growth

## Slide 74: Exponential Growth

## Slide 75: Exponential Growth

## Slide 76: Exponential Growth

## Slide 77: Exponential Growth

## Slide 78: Exponential Growth

## Slide 79: Acknowledgements
Ben West (@bewestisdoing)
Dana M. Lewis (@danamlewis) and Scott Leibrand (@scottleibrand)
Scott Hanselman (@shanselman)
Xdrip-js (@thebookins, @efidoman, @ecc1, @mhaeberli, @pietergit, @cluckj, @jpcunningh)
Milo (@sulkaharo)
Nightscout (@WeAreNotWaiting, @sulkaharo, @PieterGit, @jasoncalabrese)
T Schlussel, Andrew & B Holt, Danielle & A Crawley, Eric & B Lustik, Michael & Wade, Charles & Ft Uyehara, Catherine. (2011). Effect of Diabetes Mellitus on Outcomes of Hyperglycemia in a Mixed Medical Surgical Intensive Care Unit. Journal of diabetes science and technology. 5. 731-40. 10.1177/193229681100500328.
Dr. L.

## Slide 80: Agenda
whoami?
Introduction to Diabetes
Hardware
Software and Safety
Iterative Improvements
Live Demo
Results
Exponential Growth
Questions?

## Slide 81: Questions?
Web: https://lagor.io
Email: jay@lagor.io
Twitter: @jaylagorio
Github: @jaylagorio